## Slide 2
CLOSED END PENS
- Don Ward
Wichita Falls TX
RedRiverPens.com

## Slide 3: What is a CLOSED END PEN
A closed end pen has
no terminal hardware
?
on either the BARREL end
or on the CAP
or BOTH

## Slide 4
John Solberg
Denton TX

## Slide 5
Don Ward
Wichita Falls TX
Kit: Penache,
fromCraft Supplies
Materials: Real cigar label under CA finish

## Slide 6
Don Ward
Wichita Falls TX
Kit: Baron, aka: Navigator

## Slide 7
Blank and pen made by
JeffinIndiana . . . Shop user name

## Slide 8
Mesquite and rattlesnake skin closed end Baron.
Pen & snake blank
- Don Ward Wichita Falls, Tx

## Slide 9
Calligraphy dip pen
John Solberg
Denton, TX

## Slide 10
Calligraphy dip pens
Anthony Turchetta
Cave Creek AZ

## Slide 11
Don Ward Wichita Falls TX
Kit: Baseball Bat Pen (discontinued)

## Slide 12
Full size gavel with a closed end pen made into the gavel's handle. The kit used was the Ameri-Classic rollerball. I've also use the executive kit has been used. I now use the Baron kit for the gavel pen.
-Don Ward using mesquite

## Slide 13
Full size gavel with a closed end pen made into the gavel's handle. The kit used was the Ameri-Classic rollerball. I've also use the executive kit has been used. I now use the Baron kit for the gavel pen.
-Don Ward using mesquite

## Slide 14
Desk pen
Don Ward Wichita Falls TX
Kit: Slimline modified as
closed end and extended
in length

## Slide 15
Desk pen featured
in More Woodturning
Don Ward Wichita Falls TX
Kit: Baron aka Navigator
Wood: Mesquite

## Slide 16: Just how is the penblank held, since the hole is not a through hole, but a blind hole which has no exit . . .
?

## Slide 17
There are several ways to hold the blank. Tooling can be homemade or purchased.
One method is to use a pin chuck.

## Slide 18
In a pin chuck the pin fits into a slot and the pen tube slides over the pen.
Slightly rotating the blank will cause the pin to grab the tube and hold the blank.
A pin chuck can be made in your shop.
I don't know anyone who is currently making them to be sold.
CHUCK
PIN
PEN TUBE

## Slide 19
Homemade Jam chuck
The lower portion is shaped to fit the taper in the lathe headstock or it can be held in a Jacob's chuck or some other type of chucking system.

## Slide 20
Homemade Jam chuck
The upper portion is made for the pentube to friction fit or jam fit to hold the blank.

## Slide 21
Although not available in sizes that fit very many pen kit tubes, there are a few that will work.
A baron tube is shown
here and surprisingly
the one I tried ran
Truer than I thought
it would. There was
very little runout.
CONCRETE ANCHORS

## Slide 22
Commercially available
closed end pen mandrels:
from Arizona Silhouette in sizes
for several kits sold by them.
There is even a 7mm mandrel
which I used to make the 7mm
desk pen shown earlier.

## Slide 23
There is a method to hold a blank with a blind hole for making closed end pens that requires no special tooling. All that is needed is a mandrel and bushings.

## Slide 24
LET’S MAKE A PEN !